## Slide 1: Efficiency of an air-core induction electromagnetic linear accelerator
By Jim Garvey

## Slide 2: Overview
LabView Program
Calibration Methods
Gauss Cannon Methods
Gauss Cannon Results
Conclusion

## Slide 3: Front View of LabView Program
The Waveform graph displays the voltage reading across a photodiode. This is a
calibration step to determine the appropriate threshold voltage for measurements.

## Slide 4: Front View Recording a “Shot”

## Slide 5: LabView Block Diagram

## Slide 6: Photogate Set-up
LabView on Comp
V Out
V in
NI9263
NI9201
Infrared LED
Infrared Photodiode
Acquire Voltage
Generate Voltage
Projectile Motion

## Slide 7: Calibration Methods
2 measurements with uncertainty, the ‘width of the projectile’ and the time the projectile was in the gate.
  Width of projectile:
½ R
R
0.866R
1.7321R
∆D = +/- 0.268R

## Slide 8: Calibration Methods Cont
Uncertainty in Time experiment
  Dropped Projectile from set height from my photogate
  Used the LabView program I wrote to measure the time in the gate
  Compared to the expected value I calculated
  Gave me a percentage that I would use as my estimated uncertainty in time

## Slide 9: Calibration Methods Cont
Trial | Time in Gate
1 | 0.0117
2 | 0.0118
3 | 0.0119
4 | 0.0116
5 | 0.0121
6 | 0.0120
7 | 0.0121
8 | 0.0118
9 | 0.0119
10 | 0.0120
Equation: x(t) = X0 + V0 *t + 0.5*a*t2
drop height: 0.095m
diameter of ball: 0.016m
Want the time that the ball enters the
“beam” and when it leaves. So find
t when x = drop height – r and when
x = drop height + r
Expected time is 0.012s
Average is 0.0119
Therefore the error is ~ 1%

## Slide 10: Gauss Cannon Circuit Diagram

## Slide 11: Gauss Cannon Data Collection Methods
Positioned photogate within one centimeter from the end of the barrel of the Gauss Cannon
Charged the Capacitor to a voltage around 5V above the test voltage (DMM to measure)
Ran the LabView program when the voltage dropped to within one volt of the test voltage
Fired the cannon when the voltage reached the test voltage
Recorded the time in gate and velocity

## Slide 12: Key Equations
E = ½ C V2
  C is capacitance and V is voltage
E = ½ m v2
  M is mass and v is velocity
Error propagation is simplified because the error in the velocity is dominated by the standard deviation and I assume that the uncertainty in the voltage measured by the DMM is negligible compared to the +/- 20% Capacitance of the Capacitor
Error propagation equations: quotient rule and power rule

## Slide 13: Gauss Cannon Raw Data Example
Input Voltage(V) | Time in Gate (s) | δt (s) | Width (m) | δw (m)
150 | 0.00117 | 1E-05 | 0.026 | 0.003
150 | 0.00112 | 1E-05 | 0.026 | 0.003
150 | 0.00108 | 1E-05 | 0.026 | 0.003
150 | 0.00110 | 1E-05 | 0.026 | 0.003
150 | 0.00109 | 1E-05 | 0.026 | 0.003

## Slide 14: Gauss Cannon Results
Input V (V) | Input E (J) | δEin (J) | Velocity (m/s) | δV (m/s) | Output E (J) | δEout (J) | %Eff | δEff
100 | 34 | 6.8 | 16.41 | 1.17 | 1.948 | 0.010 | 5.7 | 1.14
150 | 76.5 | 15.3 | 23.39 | 0.70 | 3.958 | 0.004 | 5.2 | 1.04
200 | 136 | 27.2 | 26.10 | 0.82 | 4.926 | 0.005 | 3.6 | 0.72
300 | 306 | 61.2 | 29.73 | 1.11 | 6.393 | 0.009 | 2.1 | 0.42
430 | 628.7 | 125.7 | 34.29 | 4.77 | 8.5 | 0.2 | 1.4 | 0.28
Mass of the Projectile was 14.47g and its width was 0.026m. The Standard
Deviation of the velocity data dominated the uncertainty in the velocity.
Capacitance of capacitor was 6800 μF +/- 20% which dominated uncertainty in eff

## Slide 15: Gauss Cannon Results cont
Chart: 
| 100 | 150 | 200 | 300 | 430
Input Voltage | 34 | 76.5 | 136 | 306 | 628.7
Output Voltage | 1.948 | 3.958 | 4.926 | 6.393 | 8.5

## Slide 16: Credits
Kyle Werner and Peter Yaworsky who built the Gauss Cannon in the Modern Electronics Lab and made the circuit diagram